Loss, noise and two Friis equations

---
RF transceiver block diagram
Common RF transceiver includes:
- RX chain
- TX chain
- One or more antennas
Image source:
www.pasternack.com/pages/Technical-Charts/RF-Transceiver.pdf

---
RF transceiver block diagram
Common RF transceiver includes:
- RX chain
- TX chain
- One or more antennas
Image source:
www.pasternack.com/pages/Technical-Charts/RF-Transceiver.pdf

---
RF link budget
Common RF communication system consists of one or several transceivers.
It is important to determine relation between transmitted power, distance and received power to design system properly.

---
RF link budget
Friis transmission equation is often used to calculate received signal power:
where
- PRX – received power [W]
- PTX – transmitted power [W]
- DRX – receiver antenna directivity
- DTX – transmitter antenna directivity
- λ – wavelength of signal [m]
- d – distance between RX and TX [m]
P_RX= P_TX cdot D_TX cdot D_RX cdot ( {λ} over {4 π d } )^2 ,

---
RF link budget logarithmic form
Example of RF link budget calculation:
PTX = 1 W, DTX = 10, DRX = 1, d = 100 m, f=800 MHz
The logarithmic form of the equation allows you to simplify calculations, which consist of a large number of arguments and a lot of multiplications:
- W → dBm
- Ratio → dB
- Multiplication → Summation
- Division → Subtraction
P_RX= 1 cdot 10 cdot 1 cdot ( {0.375} over {4 π cdot 100 } )^2= 0.0000009 W =0.9 uW

---
RF link budget logarithmic form
Logarithmic conversion formulas:
- dB basic formula
- W → dBm conversation formula
- Friis equation logarithmic form
- Previous example in logarithmic form:
D_P = 10 cdot lg {P_2} over {P_1}
P[dBm] = 10 cdot lg {P[W]} over {0.001W}
P_RX[dBm]= P_TX[dBm] + D_TX[dB] + D_RX [dB] + ( {λ} over {4 π d } )^2[ dB ]
P_RX[dBm]= 30[ dBm ] +10[ dB]+0[ dB ]+( -70.5 )[ dB ]=-30.5[ dBm ]

---
Noise figure
Noise figure is a measure of degradation of the signal-to-noise ratio (SNR) in a signal chain.
SNR degradation on QPSK constellation
Image source:
https://docplayer.net/45205148-Dsp-based-phase-lock-loops-for-carrier-and-timing-recovery-at-low-signal-to-noise-ratio-a-thesis-presented-to-the-faculty-of.html

---
Noise figure
Noise figure formula:
NF of ideal element is 0 dB. In fact it is always >0 dB
NF = 10 cdot lg { {S_i} wideslash {N_i} } over { {S_o} wideslash {N_o} } =SNR_i[ dB ] - SNR_o[ dB ]
Image source:
https://literature.cdn.keysight.com/litweb/pdf/5952-8255E.pdf

---
Noise figure
In noise-sensitive applications low-noise amplifiers (LNA) are used.
Noise figure is usually described in amplifier datasheet.
There are 2 datasheet parameter tables for general-purpose amplifier (on the left picture) and for LNA (on the right picture) for example
Image sources:
https://www.analog.com/media/en/technical-documentation/data-sheets/hmc313.pdf
https://www.analog.com/media/en/technical-documentation/data-sheets/hmc639.pdf

---
Noise figure
Noise figure of passive device (e.g. filter, cable, switch, attenuator) is equal to its loss
For example, 4 inch long trace can attenuate Wi-Fi 5GHz signal
by 3 dB and add 3 dB noise due to noise figure
Image source:
http://signal-processing.mil-embedded.com/articles/can-pcb-handle-speed/

---
Noise figure
Friis formula for cascaded devices
where
FN is device noise factor (noise figure converted to ratio)
GN is device gain (linear, not in dB)
This formula shows that first device noise factor (i.e. noise figure) and gain are most important for overall system noise factor
G=G_1+ G_2 + G_3 + ... + G_n
F=F_1+ {F_2 - 1} over {G_1} + { F_3 - 1 } over { G_1 G_2 } + ... + { F_n - 1 } over { G_1 G_2 G_3 ... G_N } ,

---
Noise figure
Let’s consider a simple GPS-receiver input circuit consists of two elements: low noise amplifier and band-pass filter. There are two variants of cascade connection for two elements:
Noise figure of system decreased by ~2.6 dB (almost 2 times) due to components rearrangement. BTW, BPF+LNA connection has some pros (i.e. better out-of-band signal immunity)
Device	Description	NF, dB	G, dB
LNA	BGU7004 (LNA for GPS application)	0.85	16.5
Band-pass filter	SF1186B-2 (BPF for GPS application)	2.7	-2.7
(1)	LNA + BPF	0.92	13.8
(2)	BPF + LNA	3.55	13.8

---
Noise figure
Conclusions
- It is important to calculate noise figure of RX chain for noise-sensitive applications
- It is important to place LNA as close to the antenna as possible
- Active antenna can be used to reduce noise figure of receiver
- Properly designed RX chain can increase range of wireless connection and increase battery life

---
Matching networks
Complex impedance
Impedance is the measure of current response when a voltage is applied. It can be represented in a complex form:
Z = R + j cdot X
Z = R ( X=0 )
Z = j cdot ω cdot L ( R=0 )
Z = {1} over {j cdot ω cdot C} ( R=0 )
Image source:
https://en.wikipedia.org/wiki/Electrical_impedance

---
Matching networks
Complex impedance
Any system can be represented as a source with output impedance of ZS, load with impedance of ZL and a transmission line with characteristic impedance of Z0
There is an maximum power transfer theorem: to obtain maximum power from a source, the resistance of the load must equal the resistance of the source.
Image source:
https://en.wikipedia.org/wiki/Characteristic_impedance

---
Matching networks
Transmission lines
Transmission line is any structure designed to conduct AC signal at a frequency high enough that their wave nature must be taken into account.
Main parameter is characteristic impedance Z0
where V and I are voltage and current respectively of a wave propagating along the line.
Examples:
- USB-cable (90Ω impedance);
- Coaxial TV cable (75Ω impedance);
- Coaxial RF cable (50Ω impedance);
Z_0 = {V} over {I},

---
Matching networks
S-parameters
Most of RF devices (amplifier, filter, attenuator etc) can be represented as a two-port network. S-parameters show relationship between power of
incident (a1 and a2) and reflected waves (b1 and b2)
S_mn = {b_m} over {a_n}

---
Matching networks
S-parameters example
S-parameters
        - gain
        - input reflection coefficient
        - output reflection coefficient
S_21 = {b_2} over {a_1}=G
S_11 = {b_1} over {a_1}=IRC
S_22 = {b_2} over {a_2}=ORC
Image source:
https://www.analog.com/media/en/technical-documentation/data-sheets/HMC788A.pdf

---
Matching networks
Reflection coefficient
Reflection coefficient shows how much power of wave is reflected by device input.
The aim of circuit matching is to decrease reflection coefficient
Image source:
https://en.wikipedia.org/wiki/Reflection_coefficient

---
Matching networks
Smith chart
Smith chart shows element impedance normalized to desired impedance on a polar plot.
z = {Z_L} over {Z_o}
Image source:
https://en.wikipedia.org/wiki/Smith_chart

---
Matching networks
Unmatched case

---
Matching networks
L-matching network
Consists of two components connected in L-shape
Image source:
https://www.allaboutcircuits.com/textbook/radio-frequency-analysis-design/selected-topics/understanding-matching-networks/

---
Matching networks
Pi-matching network
Consists of three components connected in π-shape
Image source:
https://www.allaboutcircuits.com/tools/pi-match-impedance-matching-calculator/

---
Matching networks
Matching example

---
Matching networks
Transmission line matching
Any reactive component can be replaced with a transmission line segment (“distributed element”)
X_DISTRIBUTED = Z_0 cdot tan (2 cdot π cdot {l} over {λ} )
X_LUMPLED = ω cdot L
X_LUMPLED = {1} over {ω C}
X_DISTRIBUTED = Z_0 cdot cot (2 cdot π cdot {l} over {λ} )
X_LUMPLED = ω cdot L
X_DISTRIBUTED = Z_0 cdot sin (2 cdot π cdot {l} over {λ} )
X_LUMPLED = {1} over {ω C}

---
Matching networks
Transmission line matching

---
Noise figure
Conclusions
- Simple matching circuits (L- and Pi-pad) can provide good matching in narrow band only
- Length of transmission line is important for matching and transmission line should be taken into account at matching circuit design phase
- There is a lot of parameters which are difficult to factor at design phase so it is better to verify all RF-solutions at prototypes
- S-parameters and Smith chart can make RF-issues solving easier

---
Thank You!

---
dB conversion